## Slide 2
Current solutions:
Shipyard Characteristics
Large structures
Variable weld types
Poor fit ups
Hard to access spaces
Limit Automation & Robotics To:
Robots that can be stationary or guided
by track, adjacent surfaces or gantries
Materials that can be brought to robots
Spaces that are relatively easy to access
Background: SHIPYARD ROBOTICS CHALLENGES
Focus on improved tool for weld mechanization

## Slide 3
Recent/Continual Advances in robots
Advanced mobility
Collaborative robots
  Full 6 dof pose
  Lighter, safer, cheaper
  Enhanced sensing, actuators
Challenge with existing solutions:
High cost
Difficult to scale
Lose effectiveness as product moves out of Panel lines
Rely on accurate Cad models
Do not cope well with un-modeled staging
Limitations/opportunities
PROPOSED SOLUTION
HMMR:
High Mobility Manufacturing Robot

## Slide 4
RTT Prior Projects Addressed (RA-2017-427)
2. Robot control system and interface
1. Integration of HMMR hardware
3. Developed man-portability around shipyard
4. Automated weld-path training (using lidar mapping)
5 . Validated weld operations in 2F/3F positions (horiz./vertical fillets)
Improved weld-seam sensing to be robust to non-ideal fitup
Primary Technical Tasks
Improved weld-seam sensing and algorithms for automated weld-path training
Adaptable welding options: open-loop and closed-loop weld capability
Advanced workspace mapping for real-time obstacle avoidance
Develop supports and guides to aid in-field use
Improved operator interface and experience
Advanced Lidar options + SW

## Slide 5
Early Task Selection: Vigor Shipyards
Welding stiffeners and gussets at intersection between deckplate and bulkhead
Non-mechanized welding tasks in this region
Difficult positions to reach
Wrap-around welds require inspection and some amount of rework
Challenges

## Slide 6
Prototype Platform with Hardware (HMMR)
Modes of operation:
  Drag-through teach mode
  Teach job positioning mode
  Automatic job positioning mode
Base: Magnetic switchable
Arm: Aubo i5 commercial cobot
End-effector: Supports torch and user interface
Algorithms: Control robot motion, path and job planning
Approach:

## Slide 7
Target Job:
Welding stiffeners and gussets at intersection between deckplate and bulkhead
HMMR is man portable (approx. 50 lb)
Operator places HMMR on the flange of a stiffener approximately 2 feet from the bulkhead
Switchable magnetic base secures robot to stiffener
Preliminary Approach and Hardware
HMMR measures key points on the stiffener to teach weld path

## Slide 8
Task: T-Stiffener with gussets welds at deck plate and bulkheads
Task workspace: ~300mm (12 inch) sphere
HMMR workspace: ~ 950 mm (37 inch) sphere
HMMR positioned on stiffener
Mobility Requirements

## Slide 9
Mobile Base is magnetic switchable base to attach to top of stiffeners
To be moved by operator
Weight of Arm and base is ~50 lbs.
Prototype Mobile Base

## Slide 10
Mock-up of weld task constructed
Full-scale testing to include sensor and weld testing
Robot able to reach weld jobs with full orientation capability
Tested motion and live weld testing
Mobile Base Testing

## Slide 11
Arm Specs to meet weld requirements
Tool motions tested at 600 ipm
Axis/Joint | Range | Speed | Torque
Axis rotation base J1 | (+/-) 175 ° | 150 ° / sec | 207 Nm (153 ft-lb)
J2 axis rotation shoulder | (+/-) 175 ° | 150 ° / sec | 207 Nm(153 ft-lb)
J3 Elbow rotation axis | (+/-) 175 ° | 150 ° / sec | 207 Nm(153 ft-lb)
J4 rotation axis wrist | (+/-) 175 ° | 180 ° / sec | 34 Nm (25 ft-lb)
J5 wrist axis | (+/-) 175 ° | 180 ° / sec | 34 Nm (25 ft-lb)
J6 rotation axis wrist | (+/-) 175 ° | 180 ° / sec | 34 Nm (25 ft-lb)
Mobility Requirements for Arm:

## Slide 12
Modes of operation:
  Drag-through teach mode
  Teach job positioning mode
  Automatic job positioning mode
Base: Magnetic switchable
Arm: Aubo i5 commercial cobot
End-effector: Supports torch and user interface
Algorithms: Control robot motion, path and job planning
Prototype hardware, base + Arm + Torch:

## Slide 13
Strategies
Algorithms developed
  Path planning
  Mapping Weld path to robot frame
  Torch wire-tip sensing
  Laser-based point sensing
  Laser-base line sensing
Testing covered:
  Wrap-arounds *
  Vertical up fillets *
  Horizontal fillets*
  Teaching weld paths
  Weld Job alignment
* All welding guided by EWI
* Powerwave 450, Pulse mode, Tregassis torch
Preliminary Testing

## Slide 14
Video demonstration
https://vimeo.com/463090662/3c813a4745